## Slide 1: GENERAL STUDIES (GST211)
LECTURE NOTES
PRESENTED
TO
LEVEL 200 B.Sc. COMPUTER AND B.Sc. ZOOLOGY AND MEDICAL STUDENTS
FIRST SEMESTER,2015/2016

## Slide 2
CHEMICAL HAZARDS PRESENTED
BY
MUNIR GARBA

## Slide 3: INTRODUCTION
Human beings live with numerous hazards that threaten them.
Some hazards are related to human inventions,
Some to biological matters.
And others have to do with the type of work or activities human beings engage themselves in.

## Slide 4: What is Hazard?
A hazard is anything in the workplace that has the potential to harm people.
Hazards can include objects in the workplace, such as machinery, biological agents or dangerous chemicals.
A hazardous situation that has come to pass is called an incident.
Hazard and possibility interact together to create risk.

## Slide 5: Types of Hazards
Hazards are generally classified as one of four types, namely:
Physical,
Biological,
Ergonomic and,
Chemical.

## Slide 6: Physical hazards
Are the most common and will be present in most workplaces at one time or another.
They include unsafe conditions that can cause injury, illness and death.
Examples include:
Unguarded machinery and moving machinery parts; constant loud noise;

## Slide 7: Electrical Hazards

## Slide 8: Working from Heights (including ladders, Scaffolds, roofs, or any raised work area)

## Slide 9: Unguarded Machinery and moving machinery parts

## Slide 10: Biological hazards
Come from working with animals, people or infectious plant materials.
Work in day care, hospitals, hotel laundry and room cleaning, laboratories, veterinary offices and nursing homes may expose individual to biological hazards.

## Slide 11: Biological hazards
The types of things individual may be exposed to include:
Blood or other body fluids,
Fungi, bacteria,
Viruses, plants,
Insect bites,
Animal and bird droppings.

## Slide 12: BIOLOGICAL HARZARDS

## Slide 13: BIOLOGICAL HARZARDS

## Slide 14: BIOLOGICAL HARZARDS

## Slide 15: Ergonomic hazards
Ergonomic hazards occur when the type of work, body position and working conditions put strain on your body.
Short-term exposure may result in "sore muscles" the next day or in the days following exposure, but long term exposure can result in serious long-term injuries.
Ergonomic hazards include poor lighting, improperly adjusted workstations and chairs, frequent lifting, poor posture, awkward movements (especially if they are repetitive), having to use too much force (especially if you have to do it frequently).

## Slide 16: ERGONOMICS HAZARDS

## Slide 18: HUMAN EXPOSURE TO CHEMICALS

## Slide 19: HUMAN EXPOSURE TO CHEMICALS
Chemicals are part of everyone's life.
5-7million known
400millions tons

## Slide 20: CHEMICALS AS ADDITIVES
Each additive is assigned unique number, termed as "E numbers", which is used in Europe for all approved additives.
E100-199 Colours
E 200-297 Preservatives
E 300-385 Acidity Regulators, Anti-Oxidants, Mineral Salts
E 400-495 Vegetable Gums, Thickeners, Emulsifiers, Stabilizers
E 500-586 Mineral Salts, Anti-Caking Agents
E 620-641 Flavor Enhancers
E 900-1521 Thickeners, Vegetable Gums, Humectants, Artificial
Sweeteners

## Slide 23: HOW TOXIC CHEMICALS ENTER THE BODY

## Slide 24: Physiological Classification of Toxic Chemicals and their Effects
Irritants - refers to some sort of aggravation of whatever tissue the material comes in contact with. e.g. ammonia, nitrogen dioxide
Asphyxiants - exert their effects through a depletion of oxygen to the tissues e.g.
simple asphyxiants - carbon dioxide, nitrogen, methane, hydrogen
chemical asphyxiants - carbon monoxide, hydrogen cyanide, hydrogen sulphide.

## Slide 25: Physiological Classification of Toxic Chemicals and their Effects
Narcotics or Anaesthetics - the main toxic action is the depressant effect upon the Central Nervous System. e.g. - many organics, chloroform, xylene.
Systemic Poisons - the main toxic action includes the production of internal damage e.g. hepatotoxic agents - toxic effects produce liver damage. e.g. carbon tetrachloride.
Nephrotoxic agents - toxic effects produce kidney damage e.g. some halogenated hydrocarbons

## Slide 26: Physiological Classification of Toxic Chemicals and their Effects
Carcinogens - agents/compounds that will induce cancer in humans. e.g. benzene, arsenic, inorganic salts of chromium, nickel, beryllium. Ethidium Bromide.
Mutagens - agents that affect the cells of the exposed people in such a way that it may cause cancer in the exposed individual or an undesirable mutation to occur in some later generation. e.g. variety of chemical agents that alter the genetic message.

## Slide 27: Physiological Classification of Toxic Chemicals and their Effects

## Slide 28: Physiological Classification of Toxic Chemicals and their Effects

## Slide 29: Physiological Classification of Toxic Chemicals and their Effects
Teratogens - Agents or compounds that a pregnant woman takes into her body that generate defects in the fetus e.g. Thalidomide, possibly steroids. 13, cis-retinoic acid Isotretinoin.

## Slide 30: Physiological Classification of Toxic Chemicals and their Effects
Thoraco-omphalopagus female conjoined twins(Females)

## Slide 31: Factors that Determine the Type of Toxic Effect of a Chemical
There are a number of factors that determine the type of toxic effect a chemical can have on human beings. These factors include:
The chemical composition of the hazardous substance (certain substances are more harmful than others because of their chemical structure);
The physical form of the chemical (dust, vapour, liquid, etc.);

## Slide 32: Factors that Determine the Type of Toxic Effect of a Chemical
3.The route of entry by which the chemical gets into the body (chemicals have different routes of entry.
4.The particular tissues and organs in which the chemical collects or localizes;
5.The frequency, concentration, and length of exposure
6The worker's individual response to the chemical, which can vary a great deal from person to person

## Slide 33: The Material Safety Data Sheet (MSDS)
The material safety data sheet (MSDS) is a technical bulletin providing detailed hazard and precautionary information about a chemical.

## Slide 34: The Material Safety Data Sheet (MSDS)
The MSDS provides:
Product information
Fire and explosion precautions
Toxicology
Health effects
Recommended personal protective equipment (PPE)
Storage recommendations
Leaks and spills—recommended actions
Waste disposal recommendations
First aid

## Slide 35: Chemical Hazards Symbols and their Definitions
Flammable – A substance that will burn if exposed to an open flame.

## Slide 36: Chemical Hazards Symbols and their Definitions
Explosive – A substance that may explode if exposed to heat or flame.

## Slide 37: Chemical Hazards Symbols and their Definitions
Toxic/Poison – A substance that can lead to death if inhaled, ingested, or absorbed by the skin.

## Slide 38: Chemical Hazards Symbols and their Definitions
Environmental - A substances that are harmful to the environment. They must be disposed of properly, not washed down the drain

## Slide 39: Chemical Hazards Symbols and their Definitions
Irritant - A substance that causes inflammation upon contact with skin or mucous membranes

## Slide 40
RADIOCHEMICAL HAZARDS

## Slide 41: RADIOCHEMICAL HAZARD
What is Radioactivity?
Radioactivity is the spontaneous emission of radiation, and radiation is a way in which energy moves from one place to another.
Although radiation, if properly harnessed, is useful to human beings (in medicine, communication, electricity, etc.)
it is also very dangerous to all living things.
Radioactivity occurs when unstable nuclei of atoms decay and emit particles. These particles may have high energy and can have bad effects on living tissue.
Radiations are of two types, ionizing and non-ionizing.

## Slide 42: Types of Radiation
Radiations are of two types:
Non-ionizing Radiation
Ionizing Radiation

## Slide 43: IONIZATION RADIATION
Despite the harmful effect of ionizing radiations we take advantage of its properties to:
Generate electric power
To kill cancer cells
And in many manufacturing processes

## Slide 44: Radiation sources
Natural radiation comes from many sources including more than 60 naturally-occurring radioactive materials found in soil, water and air.
Man-made sources of radiation pollution are:

## Slide 45
Mining and Refining Radioactive Metals such as Uranium, Plutonium, Thorium etc.

## Slide 46
Production and explosion of nuclear weapons

## Slide 47
Production and explosion of nuclear power plants and fuels

## Slide 48
Medical Uses :Diagnosis or treatment of Cancer

## Slide 49: Types of Radioactive Decay
α DECAY
b DECAY
g DECAY

## Slide 50: Effects of Radiation on Humans
Radiation occurs when unstable nuclei of atoms decay and release particles.
When these particles touch various organic materials, such as tissue, damage may occur. Radiation can causes:

## Slide 51
The unit used to measure radiation dosage is the rem, which stands for roentgen equivalent in man (rem).
It represents the amount of radiation needed to produce a particular amount of damage to living tissue.
The total dose of rems determines how much harm a person suffers.

## Slide 52
1rem=0.01 sv, 1rem= 0.055%

## Slide 53
A dose of just 25 rems causes some detectable changes in blood,
Doses to near 100 rems usually have no immediate harmful effects.
Doses above 100 rems cause the first signs of radiation sickness including:
Nausea
Vomiting
Headache and
some loss of white blood cells

## Slide 54: Doses of 300 rems or more causes

## Slide 55: Doses of 300 rems or more causes

## Slide 56
Half of all people exposed to 450 rems die
Doses of 800 rems or more are always fatal
No treatment to radiation
2-14 days

## Slide 57: Radiation Survivors

## Slide 58: Radiation Survivors

## Slide 59: Radiation Survivors

## Slide 60: Radiation Survivors

## Slide 61: Effects of Types of Radiation
UV Rays
Ultra violet rays are short waves having wavelength 100-300 nm and high energy.
UV Rays 260nm

## Slide 62: How nuclear waste enters the body

## Slide 63: How nuclear waste enters the body
Radiation can also be in the air and can get deposited on people, plants, animals and soil.
People can inhale or ingest radionuclides in air, drinking water or food

## Slide 64: Reducing the effects of ionization radiation on the body
Use of radiation shielding materials. They include lead lined doors, leaded x-ray safety glass, leaded glass, lead lined door frames, lead lined view window frames, and many other lead shielding and industrial lead products

## Slide 65: Reducing the effects of ionization radiation on the body
Reducing the time of an exposure reduces the effective dose proportionally.
Proper disposal is key to protecting the public's health and safety and the quality of the environment.
Government regulation of the use of radioactive materials

## Slide 66: Radiation Hazards Symbols and their Definition
Non-Ionization Ionization Radiation Radiation Danger

## Slide 67
Thank you
for
Listening

## Slide 79: Aftermath of Atomic Bomb in Hiroshima

## Slide 80: Aftermath of Atomic Bomb in Nagasaki

## Slide 81: Aftermath of Atomic Bomb in Nagasaki
On August 9, 1945, during World War II, a United States Army Air Force plane released an atomic bomb on the Japanese city of Nagasaki. The blast destroyed about a third of the city and left an estimated 40,000 people dead or missing

## Slide 82
An aerial photograph reveals the devastation inflicted on Hiroshima, Japan, by an atomic bomb that was dropped on the city on August 6, 1945. Seventy thousand people were killed instantly, and 68 percent of the city was destroyed in the blast. The death toll eventually climbed to 200,000 due to radiation